4. What is the peak-to-peak amplitude (in volts) of the generated signal? (Hint: Use Measure Option and set the desired measurement quantities for the connected channel) (PostLab Q1)

5. What is the DC offset (in volts) of the signal? (PostLab Q2)

6. What is the frequency (in kHz) of the generated periodic signal? (PostLab Q3)

7. What is the execution speed (in kHz) of one iteration of the ’while’ loop ? (Hint: Take the measured frequency of the sinusoid and combine this information with the sample number of the oscillation that you can find in the code) (PostLab Q4)

8. What is the minimum and maximum amplitudes of the generated signal? Consequently what is the output voltage range and voltage resolution of the DAC? (PostLab Q5)